## Slide 1
Q-switched Treatment Guideline
Laser Toning Procedure
Step 1. After cleansing, if necessary, perform an anesthesia on the skin.
Step 2. Energy control
  If your skin and lesions are bright, raise the fluence.
  If your skin is dark and your lesions are dark, lower the fluence.
Step 3. Treatment area
  Treatment is performed by dividing the face into three parts, as shown on the right.
  Treat the entire face with overlapping, and focus more intensively on lesions.
Step 4.
  Repeat about 3 passes in 1064nm Q- Switch Mode(1064).
  After about 15 seconds, check the skin condition of the area where the laser was shot.
  Repeat 2 ~ 4 pass or so, if appropriate erythema is observed in the lesion, finish the procedure.
  ★ Be careful not to cause partial bleeding.(Excessive laser irradiation increases the likelihood of pigmentation.
Step 5. After procedure
  it is recommended to carry out the sedation pack for 15 to 20 minutes or to use an LED laser for skin regeneration.
  Apply humectant on treated areas frequently to help keep your skin moisturized.
2022

## Slide 2
Q-switched Treatment Guideline
★ Laser Toning procedure cautions
  It is recommended that the procedure be performed with an overlap of 50 ~ 60%.
  When treating the eyes and cheekbones, if the skin is thin and red, reduce the number of repetitions.
  Patients with high pigment levels should generally be treated with low energy.
  Patients with thicker pigment during treatment should stop the procedure, administer whitening,
  and reapply after one week.
Laser Toning
After Procedure
  It is carried out at intervals of one week.
  After 3 to 4 times, you feel a slight improvement, and after 7 to 8 times, you notice that your skin
  is noticeably improved
  After skin improvement, apply toning treatment every 1 to 2 months to maintain effectiveness.

## Slide 3
Soft Peel Procedure
Q-switched Treatment Guideline
Step 1. Before the procedure, please cleanse and remove the waste in the skin.
  * Exfoliation before the procedure can increase the treatment effect.
Step 2. Apply carbon
  Use a gauze or a brush to apply carbon thinly and uniformly to the treatment site.
  After applying the carbon, wait about 10~15 minutes to attach the carbon to the skin.
  Cover the eyebrows of the patient with a cotton swab or gauze.
Step 3. After about 10 minutes, if the carbon is properly absorbed into the skin, use dry gauze to wipe off
  the proper amount of carbon.
  * It is a process to apply Carbon thinly and uniformly. If the concentration is too dark, it reacts strongly.
Step 4. Shoot the laser.
  Set the energy in 1064nm mode .
  It is recommended that the procedure be performed with an overlap of 50%.
  As the carbon particles fly away, it removes the dead skin and promotes cellular renewal of the epidermis and dermis.
Step 5. After procedure
  it is recommended to carry out the sedation pack for 15 to 20 minutes or to use an LED laser for skin regeneration.
  Apply humectant on treated areas frequently to help keep your skin moisturized.

## Slide 4
Before epidermal lesion procedure
Q-switched Treatment Guideline
Avoid tanning before laser procedure.
Hairy areas are shaved and treated.
Do not take photosensitized drugs.
Before applying the anesthetic cream, wipe the skin of the treatment area with alcohol cotton.
Apply anesthetic cream 30 minutes before the procedure.
After the procedure, apply antibiotic ointment every morning and evening until the scab is removed.
After the procedure, flushing and swelling are observed at the site of treatment, and a scab is developed
after 3 to 5 days.
If you forcefully remove the scab, it may cause pigmentation or scarring,
so you should wait until it falls off by itself.
For prevention and treatment of PIH, apply sunscreen during the day and apply hydroquinone
in the evening if needed.
After epidermal lesion procedure

## Slide 5
End Point
Q-switched Treatment Guideline
Epidermal lesion(age spot, freckle, blemish): mild whitening
  If the lesion is seen as mild whitening immediately after 1 shot,
  it is an appropriate ending point.
* To prevent PIH and Bulla, do not repeatedly penetrate the same area with laser.
532nm
(Mild whitening)
(Excessive reaction)
Dermal lesion
Nevus of Ota: Frosting and petechiae
It is a good ending point when some
pinpoint bleeding occurs with frosting(gray)
immediately after 2-3 shots.
1064nm
(Frosting pinpoint bleeding)
(mild erythema)
Liver spots: Mild Erythema
It is a good ending point when some
mild erythema occurs immediately after
2-3 shots.

## Slide 6
Q-switched Treatment Guideline
Indication | Mode | Spot Size | Fluence (j/㎠) | Pulse rate (Hz) | pass | Treatment Interval / Times | End point
Laser Toning Melasma PIH | 1064 single | 8 | 1.0~ | 5~10 | 2~4 | Period : 1~2weeks Times : 10 | Mild erythema
PDP Toning | PDP |  | 1.8~ | 5~10 | 2~4 |  | PDP can be applied to non-reactive pigments.
Indication |  | Mode | Spot Size | Fluence (j/㎠) | Pulse rate (Hz) | pass | Treatment Interval /Time | End point
Epidermis | Freckle /Blemish | 532 single | 2~3 | 0.4~0.9 | 1 | 1 | Period : 4~6weeks Times : 1~2tiems | Mild whitening
 | Age spot | 532 single | 2~3 | 0.5~0.7 | 1 | 1 | Period : 4~6weeks Times : 1~2times | Mild whitening
 | Cafe au lait spot | 532 single | 2~3 | 0.5~0.7 | 1 | 1~2 | Period : 4~6weeks Times : 2~3times | Mild whitening
 | Nevus | 532 single | 2~3 | 1.2~ | 1 | 1 | Period : 4~6weeks Times : over3 times | Mild whitening
Dermis | Becker’s Nevus | 1064 single | 3 | 4.5~ | 1~2 | 1~2 | Period : 4~6weeks Times : over6 times | Mild erythema
 | Blue Nevus | 1064 single | 2 | 18.0~ | 1~2 | 1~2 | Period : 4~6weeks Times : over6 times | Mild erythema
 | Ota Nevus | 1064 single | 4 | 4.5~ | 1 | 1 | Period : 4~6weeks Times : 5~10 times | frosting/petechia
* Ota Navus
As the number of treatments increases, the color of the lesions becomes lighter and there are fewer pigments that absorb laser light, so reduce the flow (j/cm2) gradually.
When using Zoom H.P, Please keep the distance (2-3 cm in distance from the lesion)

## Slide 7
Indication | Mode | Spot Size | Fluence(j/㎠) | Hz | Repeatation | pass | Hand piece
Regeneration Pore Scar | 1064 single | 10 | 0.8~1 | 1~5 | 5 | 1 pass | MLA ZOOM If the symptoms are severe, stacking is performed up to 3 times. After 1 minute and 30 seconds, petechiae can be observed.
 |  | 7 | 0.88 ~ 1 |  |  |  | 
 |  | 4 | 0.87 ~ 1 |  |  |  | 
Indication | Mode | Spot Size | Fluence (j/㎠) | Hz | pass | Treatment Interval / Times | End point
Genesis | 1064 Quasi | 6 | 10.2 | 5~10 | 2~4 pass | Interval : 1~2 weeks Treatment is performed on a regular basis, depending on the condition of the face. | Mild erythema
Soft Peeling | 1064 single | 8 | 0.8~1.3 | 5~10 | After removing 1 pass carbon, apply 2 to 3 passes |  | 
Q-switched Treatment Guideline
Tattoo (black, blue) | 1064 single | 8 | 1.8~3.18 | 1~2 | 1 pass | Interval : 3~5weeks Treatment is performed on a regular basis, depending on the condition of the face. Don't overlap as much as possible. It starts with a large spot size and low energy setting. and reduce smaller spot size and increase energy from the next session. | Immediate End Point : Frosting End point after 10 minutes : Petechiae
 |  | 6 | 2~4 |  |  |  | 
 |  | 3~4 | 3~6 |  |  |  | 

## Slide 8
Indication |  | Skin Type | Handpiece | Spot Size (mm) | On Time (ms) | Fluence (J/cm2) | Frequency (Hz) | Treatment Guide
Hair Removal | Dark Skin Type | V | Zoom | 10 | 1 | 16-18 | 1 ~ 2 | 1pass overlap 18%
 |  | VI | Zoom | 10 | 1 | 14-16 | 1 ~ 2 | 
 | Fine Hair | Light | Zoom | 10 | 10 ~ 20 | 30 ~ 40 | 1 ~ 2 | Interval : 4~6weeks No overlapping Air cooling Topical Anesthesia
 |  | Dark | Zoom | 10 | 20 ~ 30 | 40 ~ 50 | 1 | 
 | Thick Hair | Light | Zoom | 10 | 30 ~ 40 | 20 ~ 30 | 1 | 
 |  | Dark | Zoom | 10 | 40 ~ 60 | 30 ~ 40 | 1 | 
Indication | Handpiece | Spot Size (mm) | On Time (ms) | Fluence (J/cm2) | Frequency (Hz) | Treatmaent Guide | 
genesis | Zoom | 6 | 0.3 | 10.6~ | 10 | 1~2weeks 2~3pass | Erythema For skin type 3 or higher, lower the fluence slightly
 |  | 5 | 0.5 | 10 ~ 15.2 | 5 ~ 10 |  | 
 |  | 7 | 5 | 0.91 ~ 20.8 | 3~4 |  | 
 |  | 10 | 30 ~ 50 | 19.7 ~ 25.4 | 1 |  | 
Tightening & Lifting |  | 10 | 40 ~ 50 | 28 ~ 50.9 | 1 | 3~4 weeks 2~3pass | 
Active Acne |  | 8 | 0.3 | 5.5~6.5 | 5-10 | 2~4weeks 1~3pass | When irradiated on a spot that has just been scarred, it turns purple, but since this reaction is a strong reaction, do not overlap. Inflamed areas are treated in 2-3 passes. Because it is a parameter that can be hair removal, avoid hairy areas. Irradiate after extraction or Triam Injection
 |  | 8 | 20 | 10~20 | 2~3 |  | 
Long pulsed Treatment Guideline

## Slide 9
Indication |  | Handpiece | Spot Size (mm) | On Time (ms) | Fluence (J/cm2) | Frequency (Hz) | Treatment Guide
Vascular Lesions | Flush (Acne Erythema) | Zoom | 5 | 0.5 | 10 ~ 15 | 5 ~ 10 | Strong Erythema Air cooling Post cooling required
 | Telangiectasia | Zoom | 2 ~ 3 | 5 | 160 ~ 180 | 1 | No Overlapping Interval : 4~8 weeks Air Cooling Topical Anesthesia
 | Low and Thin Blood Vessel | Zoom | 3~4 | 1 ~ 5 | 100 ~ 180 | 1 | Fluence : Up Pulse width : Down
Long pulsed Treatment Guideline
In the case of Long Pulse, the laser penetration depth is deep and there is a possibility of scarring, so it should be used with caution.
In particular, deep lesions in the mucous membrane may cause nerve damage and hemorrhage, so you should be especially careful.
In the case of Varicose Vein, since the blood vessel wall is tough and thick, the pulse width is longer and the fluence is higher than facial treatment.
Because strong energy is used, Additional Pre, Post-Cooling are essential.